## Slide 1: Unit-02: Physical Layer
Introduction to Physical Layer-1: Data and Signals, Digital Signals, Transmission Impairment, Data Rate Limits, Performance.
Digital Transmission: Digital to Digital Conversion (Only Line coding: Polar, Bipolar and Manchester coding), Analog to Digital conversion (only PCM), Transmission Modes.
08 hours of duration

## Slide 2: Physical Layer
The physical layer actually interacts with the transmission media.
The layer is involved in physically carrying information from one node in the network to the next.
One major task is to provide services for the data link layer.
The data in the data link layer consists of Os and I s organized into frames that are ready to be sent across the transmission medium.
This stream of Os and I s must first be converted into another entity: signals.
One of the services provided by the physical layer is to create a signal that represents this stream of bits.

## Slide 3: Data and Signals
Function: Move data in the form of electromagnetic signals across a transmission medium.
Data can be in any form, you are working with the transmission of data across network connections
Data usable to a person or application are not in a form that can be transmitted over a network.
For example, a photograph must first be changed to a form that transmission media can accept.
To be transmitted, data must be transformed to electromagnetic signals.
Both data and the signals that represent them can be either analog or digital in form

## Slide 4: Analog and digital data
Data can be analog or digital.
The term analog data refers to information that is continuous.
digital data refers to information that has discrete states.
For example, an analog clock that has hour, minute, and second hands gives information in a continuous form.
Here the movements of the hands are continuous.
A digital clock that reports the hours and the minutes will change suddenly from 8:05 to 8:06

## Slide 5: Cont..
Analog data, such as the sounds made by a human voice, take on continuous values.
someone speaks, an analog wave is created and captured by a microphone and converted to an analog signal.
Digital data take on discrete values. For example, data are stored in computer memory in the form of Os and 1s.
They can be converted to a digital signal.
Analog data are continuous and take continuous values.
Digital data have discrete states and take discrete values.

## Slide 6: Analog and digital signals
Like the data they represent, signals can be either analog or digital.
An analog signal has infinitely many levels of intensity over a period of time.
A digital signal, on the other hand, can have only a limited number of defined values.
Although each value can be any number, it is often as simple as 1 and O.
The simplest way to show signals is by plotting them on a pair of perpendicular axes
The vertical axis represents the value or strength of a signal. The horizontal axis represents time.

## Slide 7: Analog VS Digital Signals
Figure : Comparison of analog and digital signals

## Slide 8: Periodic and Non periodic signals
Both analog and digital signals can take one of two forms: periodic or nonperiodic.
A periodic signal completes a pattern within a measurable time frame, called a period, and repeats that pattern over subsequent identical periods.
The completion of one full pattern is called a cycle.
A nonperiodic signal changes without exhibiting a pattern or cycle that repeats over time.
In data communication, commonly use periodic analog signals and non periodic digital signals.

## Slide 9: Periodic analog signals
Periodic analog signals can be classified as simple or composite.
A simple periodic analog signal, a sine wave, cannot be decomposed into simpler signals.
A composite periodic analog signal is composed of multiple sine waves.

## Slide 10: Two signals with the same phase and frequency, but different amplitudes
Frequency and period are the inverse of each other.

## Slide 11: Two signals with the same amplitude and phase, but different frequencies

## Slide 12: Units of period and frequency

## Slide 13: Example-01
The power we use at home has a frequency of 60 Hz. The period of this sine wave can be determined as follows:

## Slide 14: Example-02
The period of a signal is 100 ms. What is its frequency in kilohertz?
Solution
First we change 100 ms to seconds, and then we calculate the frequency from the period (1 Hz = 10−3 kHz).

## Slide 15: Digital Signals
In addition to being represented by an analog signal, information can also be represented by a digital signal.
For example, a 1 can be encoded as a positive voltage and a 0 as zero voltage.
A digital signal can have more than two levels. we can send more than 1 bit for each level.
The figure in the next slide shows two signals, one with two levels and the other with four.
In general, if a signal has L levels, each level needs log2L bits.

## Slide 16: Two digital signals: one with two signal levels and the other with four signal levels

## Slide 17: Example
A digital signal has eight levels. How many bits are needed per level? We calculate the number of bits from the formula.
Each signal level is represented by 3 bits.

## Slide 18: Example
A digital signal has nine levels. How many bits are needed per level? We calculate the number of bits by using the formula.
Each signal level is represented by 3.17 bits. However, this answer is not realistic.
The number of bits sent per level needs to be an integer as well as a power of 2. For this example, 4 bits can represent one level.

## Slide 19: Bit Rate
Most digital signals are nonperiodic, and thus period and frequency are not appropriate characteristics.
Another term-bit rate (instead of frequency)-is used to describe digital signals.
The bit rate is the number of bits sent in 1sec, expressed in bits per second (bps).

## Slide 20: Example

## Slide 22: Example

## Slide 23: Bit Length
We discussed the concept of the wavelength for an analog signal.
The distance one cycle occupies on the transmission medium.
Similar for a digital signal: the bit length.
The bit length is the distance one bit occupies on the transmission medium.
Bit length =propagation speed x bit duration

## Slide 24: Transmission of Digital Signals
Digital signal may be periodic or non periodic.
Digital signal is a composite analog signal with frequencies between zero to infinity.
But most of the time non periodic digital signals are used.
Fundamental question is how can we send a digital signal from point A to point B.
We can transmit a digital signal by using one of two different approaches:
  Baseband Transmission.
  Broadband Transmission(Using Modulation).

## Slide 25: Baseband Transmission
Baseband transmission means sending a digital signal over a channel without changing the digital signal to an analog signal.
Baseband transmission requires that we have a low-pass channel, a channel with a bandwidth that starts from zero.
For example, the entire bandwidth of a cable connecting two computers is one single channel

## Slide 26: Baseband Transmission- Cont..
As another example, we may connect several computers to a bus, but not allow more than two stations to communicate at a time.

## Slide 27: Case 1: Low-Pass Channel with Wide Bandwidth
If we want to preserve the exact form of a nonperiodic digital signal with vertical segments vertical and horizontal segments horizontal.
we need to send the entire spectrum, the continuous range of frequencies between zero and infinity.
It is possible if we have a dedicated medium between the sender and receiver that preserves the exact amplitude of each component of the composite signal.
Coaxial cable or fiber optic, with a very wide bandwidth, two stations can communicate by using digital signals with very good accuracy

## Slide 28: Baseband transmission using a dedicated medium

## Slide 29: Baseband transmission using a dedicated medium
Although the output signal is not an exact replica of the original signal, the data can still be deduced from the received signal.
Baseband transmission of a digital signal that preserves the shape of the digital signal is possible only if we have a low-pass channel with an infinite or very wide bandwidth.

## Slide 30: Case-2: Low-Pass Channel with Limited Bandwidth
In a low-pass channel with limited bandwidth, we approximate the digital signal with an analog signal.
The level of approximation depends on the bandwidth available.
Rough Approximation: Let us assume that we have a digital signal of bit rate N.
If we want to send analog signals to roughly simulate this signal, we need to consider the worst case, a maximum number of changes in the digital signal.
Signal carries the sequence 01010101 or the sequence 10101010.
To simulate these two cases, we need an analog signal of frequency f = N/2.

## Slide 31: Cont..
Let 1 be the positive peak value and 0 be the negative peak value. We send 2 bits in each cycle;
The frequency of the analog signal is one-half of the bit rate, or N/2.
The above example is holds good for 2 pattern digital signal. Digital signal with a 3-bit pattern can be simulated by using analog signals.
The two similar cases (000 and 111) are simulated with a signal with frequency f =0 and a phase of 180° for 000 and a phase of 0° for 111.
The two worst cases (010 and 101) are simulated with an analog signal with frequencyf =N/2 and phases of 180° and 0°.
The other four cases can only be simulated with an analog signal with f = N/4 and phases of 180°, 270°, 90°, and 0°.

## Slide 32: Rough approximation of a digital signal using the first harmonic for worst case

## Slide 33: Example-01

## Slide 34: Example-02

## Slide 35: Broadband Transmission (Using Modulation)
Broadband transmission or modulation means changing the digital signal to an analog signal for transmission.
Modulation allows us to use a bandpass channel-a channel with a bandwidth that does not start from zero.
If the available channel is a bandpass channel, we cannot send the digital signal directly to the channel; we need to convert the digital signal to an analog signal before transmission.

## Slide 36: Broadband Transmission
Modulation of a digital signal for transmission on a bandpass channel.

## Slide 37: Transmission Impairment
Signals travel through transmission media, which are not perfect.
The imperfection causes signal impairment. This means that the signal at the beginning of the medium is not the same as the signal at the end of the medium.
What is sent is not what is received.
Three causes of impairment are attenuation, distortion, and noise.

## Slide 38: Attenuation
Attenuation means a loss of energy.
When a signal, simple or composite, travels through a medium, it loses some of its energy in overcoming the resistance of the medium.
That is why a wire carrying electric signals gets warm, if not hot, after a while.
Some of the electrical energy in the signal is converted to heat.
To compensate for this loss, amplifiers are used to amplify the signal.

## Slide 39: Attenuation

## Slide 40: Attenuation- Measurement
To show the loss or gain of energy the unit “decibel” is used.
The decibel (dB) measures the relative strengths of two signals or one signal at two different points.
Note that the decibel is negative if a signal is attenuated and positive if a signal is amplified.
Decibel dB = 10log10P2/P1, Where P1- Input Signal and P2 - output signal.

## Slide 41: Example-01

## Slide 42: Example-02

## Slide 43: Example-03

## Slide 44: Example-04

## Slide 45: Example-05

## Slide 46: Distortion
Distortion means that the signal changes its form or shape.
Distortion can occur in a composite signal made of different frequencies.
Each signal component has its own propagation speed through a medium and its own delay in arriving at the final destination.
In other words, signal components at the receiver have phases different from what they had at the sender.
The shape of the composite signal is therefore not the same.

## Slide 47: Distortion

## Slide 48: Noise
Several types of noise, such as thermal noise, induced noise, crosstalk, and impulse noise, may corrupt the signal.
Thermal noise is the random motion of electrons in a wire which creates an extra signal not originally sent by the transmitter.
Induced noise comes from sources such as motors and appliances.
Crosstalk is the effect of one wire on the other. One wire acts as a sending antenna and the other as the receiving antenna.
Impulse noise is a spike (a signal with high energy in a very short time) that comes from power lines, lightning, and so on.

## Slide 49: Noise

## Slide 50: Signal to Noise Ratio (SNR)
To measure the quality of a system the SNR is often used.
It indicates the strength of the signal wrt the noise power in the system.
to find the theoretical bit rate limit, we need to know the ratio of the signal power to the noise power.
It is usually given in dB and referred to as SNRdB.
The signal-to-noise ratio is defined as
SNR= Average signal power/average noise power.
We need to consider average signal and noise power because these may change with time.
SNR is actually the ratio of what is wanted (signal) to what is not wanted (noise).

## Slide 51: 2 cases- High SNR and Low SNR
A high SNR means the signal is less corrupted by noise; a low SNR means the signal is more corrupted by noise.
Because SNR is the ratio of two powers, it is often described in decibel units, SNRdB, defined as,
SNRdb = l0log10 SNR.

## Slide 52: Noiseless scenario

## Slide 53: Example-01

## Slide 54: Data Rate Limits
A very important consideration in data communications is how fast we can send data, in bits per second.
over a channel. Data rate depends on three factors:
  The bandwidth available
  The level of the signals we use
  The quality of the channel (the level of noise).
Two theoretical formulas were developed to calculate the data rate:
  one by Nyquist for a noiseless channel.
  another by Shannon for a noisy channel.

## Slide 55: Noiseless Channel: Nyquist Bit Rate
For a noiseless channel, the Nyquist bit rate formula defines the theoretical maximum bit rate.
BitRate = 2 x bandwidth x log2 L
L is the number of signals level used to represent the data and bit rate is maximum number of bits you can send in a second.
we can have any bit rate we want by increasing the number of signal levels.
But when we increase the number of signal1eve1s, we impose a burden on the receiver.
If the number of levels in a signal is just 2, the receiver can easily distinguish between a 0 and a 1.
Increasing the levels of a signal reduces the reliability of the system.

## Slide 56: Example-01

## Slide 57: Example-02

## Slide 58: Noisy Channel: Shannon Capacity
In reality, we cannot have a noiseless channel; the channel is always noisy.
In 1944, Claude Shannon introduced Shannon capacity formula, to determine the theoretical highest data rate for a noisy channel:
Capacity =bandwidth X log2 (1 +SNR)
there is no indication of the signal level, which means that no matter how many levels we have, we cannot achieve a data rate higher than the capacity of the channel.
In other words, the formula defines a characteristic of the channel, not the method of transmission.

## Slide 59: Example-01

## Slide 60: Example-02

## Slide 61: Example-03

## Slide 62: Performance
Till now we have discussed the way of transmitting data (signals) over a network and how the data behave.
One important issue in networking is the performance of the network-how good is it?
Bandwidth: Represent the capacity of the link or channel.
Two different contexts with two different measuring values: bandwidth in hertz and bandwidth in bits per second.
Bandwidth in hertz is the range of frequencies contained in a composite signal or the range of frequencies a channel can pass.
The term bandwidth can also refer to the number of bits per second that a channel, a link, or even a network can transmit.

## Slide 63: Relationship
An increase in bandwidth in hertz means an increase in bandwidth in bits per second.
The relationship depends on whether we have baseband transmission or transmission with modulation.

## Slide 64: Throughput
The throughput is a measure of how fast we can actually send data through a network.
Bandwidth in bits per second and throughput seem the same, but they are different.
A link may have a bandwidth of B bps, but we can only send T bps through this link with T always less than B.
Bandwidth is a potential measurement of a link; the throughput is an actual measurement of how fast we can send data.
For example, we may have a link with a bandwidth of 1 Mbps, but the devices connected to the end of the link may handle only 200 kbps.

## Slide 66: Latency (Delay)
The latency or delay defines how long it takes for an entire message to completely arrive at the destination from the time the first bit is sent out from the source.
latency is made of four components: propagation time, transmission time, queuing time and processing delay.
Propagation time: It measures the time required for a bit to travel from the source to the destination.
The propagation time is calculated by dividing the distance by the propagation speed.
Propagation Delay = Distance/Propagation speed

## Slide 67: Example-1

## Slide 68: Transmission Time
Transmission speed - the speed at which all the bits in a message arrive at the destination. (difference in arrival time of first and last bit).
There is a time between the first bit leaving the sender and the last bit arriving at the receiver.
The time required for transmission of a message depends on the size of the message and the bandwidth of the channel.
Transmission Delay = Message size/bandwidth bps

## Slide 69: Example-02

## Slide 70: Example-03

## Slide 71: Queuing Time
Time needed for each intermediate or end device to hold the message before it can be processed.
The queuing time is not a fixed factor; When there is heavy traffic on the network, the queuing time increases.
Intermediator nodes like router, queues the arrived messages and processes them one by one.
If there are many messages, each message will have to wait.

## Slide 72: Bandwidth-Delay Product
Bandwidth and delay are two performance metrics of a link.
The bandwidth-delay product defines the number of bits that can fill the link.
Fig: Filling the link with bits for case 1

## Slide 73: Case-2: Filling the link with bits case2

## Slide 74: Digital Transmission
A computer network is designed to send information from one point to another.
This information needs to be converted to either a digital signal or an analog signal for transmission.
Here mainly we discuss on conversion of digital data to digital signals.
Later we discuss on methods which change an analog signal to a digital signal.
Finally, we discuss transmission modes.

## Slide 75: Digital to digital conversion
We know that signals that represent data can also be digital or analog.
Digital to digital conversion represent conversion of digital data to digital signals.
The conversion involves three techniques:
  Line coding
  Block coding
  Scrambling
Line coding is always needed, block coding and scrambling may or may not be needed.

## Slide 76: Line Coding
Line coding is the process of converting digital data to digital signals.
Data may be in the form of text, number, graphical images, audio or video are stored in computer memory as sequence of bits.
Line coding converts a sequence of bits to a digital signals.
At the sender, digital data are encoded into a digital signals; at the receiver, the digital data are recreated by decoding the digital signals.

## Slide 77: Line coding and decoding

## Slide 78: Signal elements versus data elements
In data communication, our goal is to send data elements.
A data element is the smallest entity that can represent a piece of information: this is the bit.
In digital data communications, a signal element carries data elements.
A signal element is the shortest unit (timewise) of a digital signal.
Data elements are what we need to send; signal elements are what we can send.
Data elements are being carried; signal elements are the carriers.
We define a ratio r which is the number of data elements carried by each signal element.

## Slide 79: Signal element versus data element

## Slide 80: Data rate versus signal rate
The data rate defines the number of data elements (bits) sent in 1sec, bps. Often referred as bit rate.
The signal rate is the number of signal elements sent in 1sec. The unit is the baud or baud rate.
Even some times baud rate also called by pulse rate or modulation rate.
One goal in data communications is to increase the data rate while decreasing the signal rate.
Increasing the data rate increases the speed of transmission.
Decreasing the signal rate decreases the bandwidth requirement.

## Slide 81: Relationship
Relationship between data rate vs baud rate: The relation depends on value of r.
It also depends on the data pattern.
If we have a data pattern of all 1s or all Os, the signal rate may be different from a data pattern of alternating Os and Is.
To derive a formula for the relationship, we need to define three cases: the worst, best, and average.
The worst case is when we need the maximum signal rate.
The best case is when we need the minimum.
In data communications, we are usually interested in the average case.

## Slide 82: Data rate vs signal rate
The baud or signal rate can be expressed as:
S = c x N x 1/r bauds
where N is data rate(bps), c is the case factor (worst, best & avg.) , r is the ratio between data element & signal element.

## Slide 83: Line coding schemes

## Slide 84: Unipolar scheme
All signal levels are on one side of the time axis - either above or below
NRZ - Non Return to Zero scheme is an example of this code. The signal level does not return to zero during a symbol transmission.
It has no synchronization or any error detection. It is simple but costly in power consumption.

## Slide 85: Polar- NRZ scheme
The voltages are on both sides of the time axis.
Polar NRZ scheme can be implemented with two voltages. E.g. +V for 1 and -V for 0.
There are two versions:
NRZ - Level (NRZ-L) - positive voltage for one symbol and negative for the other
NRZ - Inversion (NRZ-I) - the change or lack of change in polarity determines the value of a symbol. E.g. a “1” symbol inverts the polarity a “0” does not.
In NRZ-L the level of the voltage determines the value of the bit. In NRZ-I the inversion or the lack of inversion determines the value of the bit.

## Slide 86: NRZ-L and NRZ-I scheme

## Slide 87: Polar- RZ scheme
The Return to Zero (RZ) scheme uses three voltage values. +, 0, -.
Each symbol has a transition in the middle. Either from high to zero or from low to zero.
This scheme has more signal transitions (two per symbol) and therefore requires a wider bandwidth.
More complex as it uses three voltage level. It has no error detection capability.

## Slide 88: Polar Biphase- Manchester and Differential Manchester
Manchester coding consists of combining the NRZ-L and RZ schemes.
Every symbol has a level transition in the middle: from high to low or low to high. Uses only two voltage levels.
Differential Manchester coding consists of combining the NRZ-I and RZ schemes.
Every symbol has a level transition in the middle. But the level at the beginning of the symbol is determined by the symbol value. One symbol causes a level change the other does not.

## Slide 89: Biphase: Manchester and differential Manchester schemes

## Slide 90: Bipolar - AMI and Pseudoternary
Code uses 3 voltage levels: - +, 0, -, to represent the symbols (note not transitions to zero as in RZ).
Voltage level for one symbol is at “0” and the other alternates between + & -.
Bipolar Alternate Mark Inversion (AMI) - the “0” symbol is represented by zero voltage and the “1” symbol alternates between +V and -V.
Pseudoternary is the reverse of AMI.

## Slide 91: ANALOG-TO-DIGITAL CONVERSION
Some times we have an analog signal such as one created by a microphone or camera.
Digital data has superiority over analog signal, hence need to convert the analog signal to digital signal before transmitting.
Two techniques are used to convert the analog signal to digital signal and convert the digital signal to digital data for usage purpose:
  Pulse code modulation(PCM)
  Delta Modulation.

## Slide 92: Pulse Code Modulation-PCM
The most common technique to change an analog signal to digital data (digitization) is called pulse code modulation (PCM).
A PCM encoder has three processes, as shown in Figure

## Slide 93: Sampling
The analog signal is sampled every Ts s, where Ts is the sample interval or period.
The sampling process is sometimes referred to as pulse amplitude modulation (PAM).
After the sampling the result is still an analog signal with nonintegral values.
3 types of sampling- Ideal, Natural, and Flat-top

## Slide 94: Sampling methods
In ideal sampling, pulses from the analog signal are sampled.
This is an ideal sampling method and cannot be easily implemented.
In natural sampling, a high-speed switch is turned on for only the small period of time when the sampling occurs.
The result is a sequence of samples that retains the shape of the analog signal.
The most common sampling method, called sample and hold, however, creates flat-top samples by using a circuit.

## Slide 95: Quantization
The result of sampling is a series of pulses with amplitude values between the maximum and minimum amplitudes of the signal.
The set of amplitudes can be infinite with nonintegral values between the two limits.
These values cannot be used in the encoding process.
We need to map the infinite amplitude values onto a finite set of known values.
This is achieved by dividing the distance between min and max into L zones, each of height 
 = (max - min)/L

## Slide 96: Steps in quantization
We assume that the original analog signal has instantaneous amplitudes between Vmin and Vmax
We divide the range into L zones, each of height (delta).
We assign quantized values of 0 to L - I to the midpoint of each zone.
We approximate the value of the sample amplitude to the quantized values.

## Slide 97: Encoding
After each sample is quantized and the number of bits per sample is decided, each sample can be changed to an llb-bit code word.

## Slide 98: Transmission Modes
primary concern when we are considering the transmission of data from one device to another is the wiring.
primary concern when we are considering the wiring is the data stream. Do we send 1 bit at a time; or do we group bits into larger groups.
The transmission of binary data across a link can be accomplished in either parallel or serial mode.
In parallel mode, multiple bits are sent with each clock tick. In serial mode, 1 bit is sent with each clock tick.
While there is only one way to send parallel data, there are three subclasses of serial transmission: asynchronous, synchronous, and isochronous

## Slide 99: Data Transmission and Modes

## Slide 100: Parallel Transmission
Binary data, consisting of Is and Os, may be organized into groups of n bits each.
The mechanism for parallel transmission is a conceptually simple one: Use n wires to send n bits at one time.
Each bit has its own wire, and all n bits of one group can be transmitted with each clock tick from one device to another.
Typically, the eight wires are bundled in a cable with a connector at each end.

## Slide 101: Serial Transmission
In serial transmission one bit follows another, so we need only one communication channel rather than n to transmit data between two communicating devices
The advantage of serial over parallel transmission is that with only one communication channel, serial transmission reduces the cost of transmission.

## Slide 102: AsynchronousTransmission
In asynchronous transmission, we send 1 start bit (0) at the beginning and 1 or more stop bits (1s) at the end of each byte. There may be a gap between each byte.
Asynchronous here means “asynchronous at the byte level,” but the bits are still synchronized; their durations are the same.

## Slide 103: Synchronous transmission
In synchronous transmission, we send bits one after another without start or stop bits or gaps. It is the responsibility of the receiver to group the bits. The bits are usually sent as bytes and many bytes are grouped in a frame. A frame is identified with a start and an end byte.

## Slide 104: Isochronous transmission
In real-time audio and video, in which uneven delays between frames are not acceptable, synchronous transmission fails.
For example, TV images are broadcast at the rate of 30 images per second; they must be viewed at the same rate.
If each image is sent by using one or more frames, there should be no delays between frames.
For this type of application, synchronization between characters is not enough; the entire stream of bits must be synchronized.
The isochronous transmission guarantees that the data arrive at a fixed rate.